## Slide 1
ACADs (08-006) Covered
Keywords
Titrations, chemical separations, distillation, carrier use, gravimetric determinations, fusing, precipitation, sample fixing, concentration techniques, preparation of standard solutions
Description
Explain and apply the concepts related to water chemistry techniques.
Perform the following wet chemistry techniques.
Supporting Material
WATER CHEMISTRY TECHNIQUES
4.26.1.1 | 4.26.1.2 | 4.26.1.3 | 4.26.1.4 | 4.26.1.5 | 4.26.1.7 | 4.26.1.8 | 4.26.1.9
4.26.1.10 | 4.26.1.11 |  |  |  |  |  | 

## Slide 2: titrations
quantitative measurement of an analyte in solution by completely reacting it with a reagent solution.
Notes: Manual titration is done with a buret.
For repetitive titrations, autotitrators with microprocessors are available that deliver the titrant, stop at the endpoint, and calculate the concentration of the analyte.
http://www.files.chem.vt.edu/chem-ed/titration/titratn.html
Titration
Introduction
Titration is the quantitative measurement of an analyte in solution by completely reacting it with a reagent solution. The reagent is called the titrant and must either be prepared from a primary standard or be standardized versus a primary standard to know its exact concentration.
The point at which all of the analyte is consumed is the equivalence point. The number of moles of analyte is calculated from the volume of reagent that is required to react with all of the analyte, the titrant concentration, and the reaction stoichiometry.
The equivalence point is often determined by visual indicators are available for titrations based on acid-base neutralization, complexation, and redox reactions. and is determined by some type of indicator that is also present in the solution. For acid-base titrations, indicators are available that change color when the pH changes. When all of the analyte is neutralized, further addition of the titrant causes the pH of the solution to change causing the color of the indicator to change.
Instrumentation
Manual titration is done with a buret, which is a long graduated tube to accurately deliver amounts of titrant. The amount of titrant used in the titration is found by reading the volume of titrant in the buret before beginning the titration and after reaching the endpoint. The difference in these readings is the volume of titrant to reach the endpoint. The most important factor for making accurate titrations is to read the buret volumes reproducibly. The figure shows how to do so by using the bottom of the meniscus to read the reagent volume in the buret.
The end point can be determined by an indicator as described above or by an instrumental method. The most common instrumental detection method is potentiometricdetection. The equivalence point of an acid-base titration can be detected with a pH electrode. Titrations, such as complexation or precipitation, involving other ions can use an ion-selective electrode (ISE). UV-vis absorption spectroscopy is also common, especially for complexometric titrations where a subtle color change occurs.
For repetitive titrations, autotitrators with microprocessors are available that deliver the titrant, stop at the endpoint, and calculate the concentration of the analyte. The endpoint is usually detected by some type of electrochemical measurement. Some examples of titrations for which autotitrators are available include:
Acid or base determination by pH measurement with potentiometric detection.
Determination of water by Karl Fischer reagent (I2 and SO2 in methyl alcohol and pyridine) with coulometric detection.
Determination of Cl in aqueous solution with phenylarsene oxide using amperometric detection.

## Slide 3: chemical separations
Oxidation-Reduction Processes
Complexation
Solvent Extraction
Volatilization and Distillation
Electrodeposition
Chromatography
Precipitation and Coprecipitation
Carriers and Tracers
Notes: SEPARATION TECHNIQUES (pdf) – MARLAP , JULY 2004

## Slide 4: distillation
The separation of a volatile component(s) of a mixture by vaporization at the boiling point of the mixture and subsequent condensation of the vapor.
Essentially takes advantage of the differences in the boiling points of the constituents to separate a mixture into its components.
Notes: SEPARATION TECHNIQUES (pdf) – MARLAP , JULY 2004
14.5 Volatilization and Distillation
14.5.1 Introduction
Differences in vapor pressures of elements or their compounds can be exploited for the
separation of radionuclides. Friedlander et al. (1981), describes the process:
“The most straightforward application is the removal of radioactive rare gases from aqueous solutions or melts by sweeping an inert gas or helium. The volatility of ... compounds ... Can be used to effect separations ... By distillation ... Distillation and volatilization methods often give clean separations, provided that proper precautions are taken to avoid contamination of the distillate by spray or mechanical entrapment. Most volatilization methods can be done without specific carriers, but some nonisotopic carrier gas might be required. Precautions are sometimes necessary to avoid loss of volatile radioactive substances during the dissolving of irradiated targets or during irradiation itself.”
Similar precautions are also advisable during the solubilization of samples containing volatile elements or compounds (Chapter 13, Sample Dissolution).
14.5.3 Distillation Principles
Distillation is the separation of a volatile component(s) of a mixture by vaporization at the
boiling point of the mixture and subsequent condensation of the vapor. The vapor produced on boiling the mixture is richer in the more volatile component.the component with the higher vapor pressure (partial pressure) and correspondingly lower boiling point. The process of distillation, therefore, essentially takes advantage of the differences in the boiling points of the constituents to separate a mixture into its components. It is a useful separation tool if the analyte is volatile or can be transformed into a volatile compound. Most inorganic applications of distillation involve batch distillation, whereas most organic applications require some type of fractional distillation. In a simple batch distillation, the sample solution containing a single volatile component or components with widely separated boiling points is placed in a distillation flask, boiling is initiated, and the vapors are then continuously removed, condensed, and collected. Mixtures containing multiple volatile components require fractional distillation, which employs repeated vaporization-condensation cycles for separation, and is commonly performed in a fractionation column for that purpose. The column allows the cycles to occur in one operation, and the separated component is collected after the last condensation.
Distillation has been widely used for separating organic mixtures but this approach has less
applicability in inorganic analysis (Korkisch, 1969). Korkisch (1969) states: .Nevertheless, some of the elements of interest to radiochemists can be very effectively separated by distillation as their volatile chlorides, bromides, and oxides .... [T]hese elements are germanium (Ge), selenium (Se), technetium (Tc), rhenium (Re), ruthenium (Ru), and osmium (Os).. (Also see DOE, 1997, Method RP530). Two common analytes determined through distillation, tritium and 226Ra, by radon emanation are discussed below.
Specific distillation principles are commonly found in chemistry reference and textbooks. For a theoretical discussion of distillation see Peters (1974) and Perry and Weisberger (1965).
Distillation procedures are discussed for many inorganic applications in Dean (1995) and for less common radioanalytes in DeVoe (1962) and Kuska and Meinke (1961).

## Slide 5: carrier use
Carrier: use of a material that is different in isotopic make-up to the analyte and that raises the effective concentration of the material to the macro level.
Isotopic Carriers
Nonisotopic Carriers
Common Carriers
Holdback Carriers
Yield of Isotopic Carriers
Notes: SEPARATION TECHNIQUES (pdf) – MARLAP , JULY 2004
14.9.2 Carriers
The key to radiochemical analysis of samples with multiple radionuclides is effective separation
of the different analytes. Separations are most easily accomplished when performed on a macro
scale. As described above, however, the analytes are frequently at levels that challenge the
analyst and the conventional methods to perform the separations. The use of a material that is
different in isotopic make-up to the analyte and that raises the effective concentration of the
material to the macro level is referred to as a carrier. In many cases, the carrier is a nonradioactive
isotope of the analyte. Some carriers are stable isotopes of chemically similar elements.
A distinction exists between traditional and radiochemical analyses when referring to macro
amounts. Generally, carriers are present in quantities from a few tenths to several hundred
milligrams of material during the progress of the radiochemical separation.
14.9.2.1 Isotopic Carriers
14.9.2.2 Nonisotopic Carriers
14.9.2.3 Common Carriers
14.9.2.4 Holdback Carriers
14.9.2.5 Yield of Isotopic Carriers

## Slide 6: gravimetric determinations
Quantitative determination of an analyte based on the mass of a solid.
4 fundamental types of gravimetric analysis:
  physical gravimetry
  thermogravimetry
  precipitative gravimetric analysis
  electrodeposition
Notes: http://www.ecs.umass.edu/cee/reckhow/courses/572/572bk15/572BK15.html
CHAPTER XV: GRAVIMETRIC METHODS

## Slide 7: fusing
Accomplished by heating a salt (the flux) mixed with an appropriate amount of sample.
Mixture is heated to a temperature above the melting point of the salt, and the sample is allowed to react in the molten mixture.
When the reaction is completed, the mixture is allowed to cool to room temperature.
The fused sample is then dissolved, and the analysis is continued.
Notes: SAMPLE DISSOLUTION (pdf) – MARLAP , JULY 2004
13.3 Fusion Techniques
Sample decomposition through fusion is employed most often for samples that are difficult to dissolve in acids such as soils, sludges, silicates, and some metal oxides. Fusion is accomplished by heating a salt (the flux) mixed with an appropriate amount of sample. The mixture is heated to a temperature above the melting point of the salt, and the sample is allowed to react in the molten mixture. When the reaction is completed, the mixture is allowed to cool to room temperature. The fused sample is then dissolved, and the analysis is continued. Any residue remaining may be treated by repeating the fusion with the same salt, performing a fusion with a different salt, acid treatment, or any combination of the three.
Decomposition of the sample matrix depends on the high temperatures required to melt a flux salt and the ratio of the flux salt to the sample. For a fusion to be successful, the sample must contain chemically bound oxygen as in oxides, carbonates, and silicates. Samples that contain no chemically bound oxygen, such as sulfides, metals, and organics, must be oxidized before the fusion process.
Samples to be fused should be oven-dried to remove moisture. Samples with significant amounts of organic material are typically dry ashed or wet ashed before fusion. Solid samples are ground to increase the surface area, allowing the fusion process to proceed more readily. The sample must be mixed thoroughly with the flux in an appropriate ratio. Generally, the crucible should never be more than half-filled at the outset of the fusion process. Fusions may be performed using sand or oil baths on a hot plate, in a muffle furnace, or over a burner. Crucibles are made of platinum, zirconium, nickel, or porcelain (Table 13.1). The choice of heat source and crucible material generally depends on the salt used for the fusion.
During fusion, samples are heated slowly and evenly to prevent ignition of the sample before the reaction with the molten salt can begin. It is especially important to raise the temperature slowly when using a gas flame because the evolution of water and gases is a common occurrence at the beginning of the fusion, and hence a source of spattering. The crucible can be covered with a lid as an added precaution. Sand and oil baths provide the most even source of heat, but they are difficult to maintain at very high temperatures. Muffle furnaces provide an even source of heat, but when using them it is difficult to monitor the progress of the reaction and impossible to work with the sample during the fusion. Burners are used often as a convenient heat source although they make it difficult to heat the sample evenly.
The maximum temperature employed varies considerably and depends on the sample and the flux. In order to minimize attack of the crucible and decomposition of the flux, excessive temperatures should be avoided. Once the salt has melted, the melt is swirled gently to monitor the reaction. The fusion continues until visible signs of reaction are completed (e.g., formation of gases, foaming, fumes). It is frequently difficult to decide when heating should be discontinued. In ideal cases, a clear melt serves to indicate the completeness of sample decomposition. In other cases, it is not as obvious, and the analyst must base the heating time on past experience with the sample type.
The melt sometimes is swirled during cooling to spread it over the inside of the crucible. Thin layers of salt on the sides of the crucible often will crack and flake into small pieces during cooling. These small fragments are easier to remove and dissolve.
After the sample has returned to room temperature, the fused material is dissolved. The solvent is usually warm water or a dilute acid solution, depending on the salt. For example, dilute acid typically would not be used to dissolve a carbonate fusion because of losses to spray caused by release of CO2. The aqueous solution from the dissolution of the fusion melt should be examined carefully for particles of undissolved sample. If undissolved particles are present, they should be separated from solution by centrifugation or filtration, and a second fusion should be performed.
Several types of materials are used for crucibles, but platinum, other metals (Ni, Zr, Ag), and graphite are most common. Graphite crucibles are a cost-effective alternative to metal crucibles; they are disposable, which eliminates the need for cleaning and the possibility of cross-sample contamination. Graphite crucibles are chemically inert and heat-resistant, although they do oxidize slowly at temperatures above 430 EC. Graphite is not recommended for extremely lengthy fusions or for reactions where the sample may be reduced. Platinum is probably the most commonly used crucible material. It is virtually unaffected by most of the usual acids, including hydrofluoric, and it is attacked only by concentrated phosphoric acid at very high temperatures, and by sodium carbonate. However, it dissolves readily in mixtures of hydrochloric and nitric acids (aqua regia), nitric acid containing added chlorides, or chlorine water or bromine water. Platinum offers adequate resistance toward molten alkali metal, borates, fluorides, nitrates, and bisulfates. When using a platinum crucible, one should avoid using aqua regia, sodium peroxide, free elements (C, P, S, Ag, Bi, Cu, Pb, Zn, Se, and Te), ammonium, chlorine and volatile chlorides, sulfur dioxide, and gases with carbon content. Platinum crucibles can be cleaned in boiling HNO3, by hand cleaning with sea sand or by performing a blank fusion with sodium hydrogen sulfate.
Many kinds of salts are used in fusions. The lowest melting flux capable of reacting completely with the sample is usually the optimum choice. Basic fluxes, such as the carbonates, the hydroxides, and the borates, are used to attack acidic materials. Sodium or potassium nitrate may be added to furnish an oxidizing agent when one is needed, as with the sulfides, certain oxides, ferroalloys, and some silicate materials. The most effective alkaline oxidizing flux is sodium peroxide; it is both a strong base and a powerful oxidizing agent. Because it is such a strong alkali, sodium peroxide is often used even when no oxidant is required. Alternatively, acid fluxes are the pyrosulfates, the acid fluorides, and boric acids. Table 13.1 lists several types of fusions, examples of salts used for each type of fusion, and the melting points of the salts.
SULFATE FUSION is useful for the conversion of ignited oxides to sulfates, but is generally an ineffective approach for silicates. Sulfate fusion is particularly useful for BeO, Fe2O3, Cr2O3, MoO3, TeO2, TiO2, ZrO2, Nb2O5, Ta2O5, PuO2, and rare earth oxides (Bock, 1979). Pyrosulfate fusions are prepared routinely in the laboratory by heating a mixture of sodium or potassium sulfate with a stoichiometric excess of sulfuric acid:
Na2SO4 + H2SO4 6 [2NaHSO4] 6 Na2S2O7 + H2O
Na2S2O7 6 Na2SO4 + SO38
Na2SO4 etc.
The rate of heating is increased with time until the sulfuric acid has volatilized and a clear pyrosulfate fusion is obtained. A pyrosulfate melt can be reprocessed if necessary to achieve complete sample dissolution. The analyst must distinguish between insoluble material that has not yet or will not dissolve, and material that has precipitated during the final stages of a prolonged pyrosulfate fusion. In the latter situation the fusion must be cooled, additional sulfuric acid added, and the sample refused until the precipitated material redissolves and a clear melt is obtained. Otherwise, the precipitated material will be extremely difficult, if not impossible, to dissolve in subsequent steps. Platinum or quartz crucibles are recommended for this type of fusion, with quartz being preferred for analysis of the platinum group metals. After the melt is cooled and solidified, it should be dissolved in dilute sulfuric or hydrochloric acid rather than in water to avoid hydrolysis and precipitation of Ti, Zr, etc. Niobium and tantalum may precipitate even in the presence of more concentrated acid. In order to avoid precipitation of Nb or Ta, concentrated sulfuric acid, tartaric acid, ammonium oxalate, hydrogen peroxide, or hydrofluoric acid must be used. Mercury and the anions of volatile acids are largely volatilized during these fusion procedures.

## Slide 8: precipitation
Used to isolate and collect a specific radionuclide from other (foreign) ions in solution by forming an insoluble compound.
Accomplished by combining a selected ion(s) in solution with a suitable counter-ion in sufficient concentrations to exceed the solubility of the resulting compound and produce a supersaturated solution.
Notes: SEPARATION TECHNIQUES (pdf) – MARLAP , JULY 2004
14.8 Precipitation and Coprecipitation
14.8.1 Introduction
Two of the most common and oldest methods for the separation and purification of ions in radioanalytical chemistry are precipitation and coprecipitation. Precipitation is used to isolate and collect a specific radionuclide from other (foreign) ions in solution by forming an insolublecompound. Either the radionuclide is precipitated from solution itself, or the foreign ions are precipitated, leaving the radionuclide in solution. Sometimes a radionuclide is present in solution at sub-micro concentrations, i.e., levels so low that the radionuclide will not form an insoluble compound upon addition of a counter-ion. In these cases, the radionuclide can often be brought down from solution by coprecipitation, associating it with an insoluble substance that precipitates from solution. This phenomenon is especially important in gravimetric analysis and radiochemistry. In gravimetric analysis, carrying down of impurities is a problem. For radiochemists, coprecipitation is a valuable tool.
14.8.3 Precipitation
Precipitation is accomplished by combining a selected ion(s) in solution with a suitable counterion in sufficient concentrations to exceed the solubility of the resulting compound and produce a supersaturated solution. Nucleation occurs and growth of the crystalline substance then proceeds in an orderly manner to produce the precipitate (see Section 14.8.3.1, .Solubility and the Solubility Product Constant, Ksp.). The precipitate is collected from the solvent by a physical method, such as filtration or centrifugation. A cation (such as Sr+2, for example) will precipitate from an aqueous solution in the presence of a carbonate anion, forming the insoluble compound, strontium carbonate (SrCO3), when sufficient concentrations of each ion are present in solution to exceed the solubility of SrCO3. The method is used to isolate and collect strontium from water for radioanalysis (EPA, 1984).
A precipitation process should satisfy three main requirements:
. The targeted species should be precipitated quantitatively.
. The resulting precipitate should be in a form suitable for subsequent handling; it should be easily filterable and should not creep.
. If it is used as part of a quantitative scheme, the precipitate should be pure or of known purity at the time of weighing for gravimetric analysis.
Precipitation processes are useful in several different kinds of laboratory operations, particularly gravimetric yield determinations.as a separation technique and for preconcentration to eliminate interfering ions, or for coprecipitation.

## Slide 9: sample fixing (preservation)
Methods of preservation are relatively limited, intended generally to
  (1) retard biological action
  (2) retard hydrolysis of chemical compounds and complexes
  (3) reduce volatility of constituents
  (4) reduce absorption effects.
Preservation methods are generally limited to pH control, chemical addition, refrigeration, and freezing.
Notes: http://sisbl.uga.edu/epatab1.html
RECOMMENDATION FOR SAMPLING AND PRESERVATION OF SAMPLES, ARRANGED ACCORDING TO MEASUREMENT
Complete and unequivocal preservation of samples, either domestic sewage, industrial wastes, or natural waters, is a practical impossibility. Regardless of the nature of the sample, complete stability for every constituent can never be achieved. At best, preservation techniques can only retard the chemical and biological changes that inevitably continue after the sample is removed from the parent source. The changes that take place in a sample are either chemical or biological. In the former case, certain changes occur in the chemical structure of the constituents that are a function of physical conditions. Metal cations may precipitate as hydroxides or form complexes with other constituents; cations or anions may change valence states under certain reducing or oxidizing conditions; other constituents may dissolve or volatilize with the passage of time. Metal cations may also adsorb onto surfaces (glass, plastic, quartz, etc.), such as, iron and lead. Biological changes taking place in a sample may change the valence of an element or a radical to a different valence. Soluble constituents may be converted to organically bound materials in cell structures, or cell lysis may result in release of cellular material into solution. The well known nitrogen and phosphorus cycles are examples of biological influence on sample composition. Therefore, as a general rule, it is best to analyze the samples as soon as possible after collection. This is especially true when the analyze concentration is expected to be in the low ug/1 range.
Methods of preservation are relatively limited and are intended generally to (1) retard biological action, (2) retard hydrolysis of chemical compounds and complexes, (3) reduce volatility of constituents, and (4) reduce absorption effects. Preservation methods are generally limited to pH control, chemical addition, refrigeration, and freezing.
The recommended preservative for various constituents is given in Table 1. These choices are based on the accompanying references and on information supplied by various E.P.A. Quality Assurance Coordinators. As more data become available, these recommended holding times will be adjusted to reflect new information. Other information provided in the table is an estimation of the volume of sample required for the analysis, the suggested type of container, and the maximum recommended holding times for samples properly preserved.

## Slide 10: concentration techniques
Wide variety of methods for preconcentration and separation of trace elements, including:
Evaporation
Freezing
Coprecipitation
Flotation
Extraction
Sorption
Electrolysis
Notes: http://pdf.lookchem.com/pdf/22/5dbaf76b-67aa-4ff0-8bf4-8b036f46275d.pdf

## Slide 11: concentration techniques
Solvent Extraction
Purposes:
i) Preconcentration of trace elements
ii) Elimination of matrix interference
iii) Differentiation of chemical species.
Notes: http://prr.hec.gov.pk/Chapters/736S-2.pdf
CHAPTER – 2
SOLVENT EXTRACTION

## Slide 12: concentration techniques
Solvent Extraction
Techniques:
Batchwise single stage extractions
Multistage countercurrent continuous processes
Extraction without chemical change
Solvation mechanism
Ion exchange mechanism
Ion pair extraction
Aqueous two-phase extraction
Notes: http://en.wikipedia.org/wiki/Liquid%E2%80%93liquid_extraction

## Slide 13: preparation of standard solutions
Two common types:
Molar solutions
Normal solutions
Notes: HOW TO MAKE STANDARD SOLUTIONS FOR CHEMISTRY, by Phillip Bigelow
Both of these solutions are concentrations (or “strengths”) of a particular component
(solute) that is dissolved in a solvent.
Making a Molar solution usually involves fewer mental steps than does making a Normal
solution.

## Slide 14: preparation of standard solutions
MAKING MOLAR (M) SOLUTIONS
1 Molar solution (1M) contains 1 mole of solute dissolved in a solution totaling 1 liter.
A mole is the molecular weight (MW) expressed in grams (sometimes referred to as the ‘gram molecular weight’ (gMW) of a chemical).
Thus, 1 M = 1 gMW of solute per liter of solution.
Notes: HOW TO MAKE STANDARD SOLUTIONS FOR CHEMISTRY, by Phillip Bigelow
PART 1: MAKING MOLAR (M) SOLUTIONS
A 1 Molar solution (1M) contains 1 mole of solute dissolved in a solution totaling 1 liter.
If you use water as the solvent, it must be distilled and deionized. Do not use tap water.
A mole is the molecular weight (MW) expressed in grams (sometimes referred to as the
‘gram molecular weight’ (gMW) of a chemical). Thus, 1 M = 1 gMW of solute per liter
of solution.
Problem: How much sodium chloride is needed to make 1 liter of an aqueous 1 M
solution?
Answer:
First, we calculate the molecular weight (MW) of sodium chloride. Checking the
Periodic Table of Elements, we find that the atomic weight of sodium (Na) is 23 and the
atomic weight of chlorine (Cl) is 35.5.

## Slide 15: preparation of standard solutions
MAKING NORMAL SOLUTIONS (N)
"1 Normal" solution (1 N) contains 1 “gram equivalent weight” (gEW) of solute, topped-off to one liter of solution.
N = Weight of solute /
[milliequivalent weight of solute × Volume (in ml) of dilution]
Notes: HOW TO MAKE STANDARD SOLUTIONS FOR CHEMISTRY, by Phillip Bigelow
PART 2: MAKING NORMAL SOLUTIONS (N)
Compared to making Molar solutions, making Normal solutions can be a bit confusing.
Aqueous solutions of acids and bases are often described in terms of their normality
rather than their molarity. In order to properly make a Normal solution, the worker must
understand the difference between a pure reagent and a diluted reagent.
A "1 Normal" solution (1 N) contains 1 “gram equivalent weight” (gEW) of solute,
topped-off to one liter of solution. The gram equivalent weight is equal to the solute’s
molecular weight, expressed as grams, divided by the valence (n) of the solute:
Equivalent weight (EW) = molecular weight
_____________
n
After the equivalent weight (or millieqiuvalent weight) has been calculated, then the
following equation is used:
Weight of solute
N = __________________________________________________
milliequivalent weight of solute × Volume (in ml) of dilution
The equivalent weight (or milliequivalent weight) of a substance depends upon the type
of reaction in which the substance is taking part. Some different types of chemical
reactions, along with how to determine a solute’s equivalent weight for each reaction, are
given below.